## Slide 1: e-VTOL Flying Testbed
Sam Drury
03/12/2020
Supervisor:
Dr Sam Grimshaw
Whittle Laboratory
https://www.bellflight.com/products/bell-nexus

## Slide 2: Benefits of Ducted Fans vs Propellors
Ducted Fans can improve hovering performance compared to propellors while being safer and quieter
Notes: Electric Vertical Take off+landing veh seen as one of the Great emerging technologies of the time
Market size expected to quadruple by 2025
https://www.marketresearchfuture.com/reports/evtol-aircraft-market-7952
High speed commuting, traffic-free
Quieter and cheaper than heli
Zero emission local electric power
Scope to cost same/mile as other ride sharing platforms
Even greater benefits can be envisaged using DUCTED FANS

## Slide 3: Devising a Suitable Performance Metric
Notes: Pereira/CV analysis
Greater diffusion, less KE loss – limit due to adv P causing BL separation, not as much pressure recovery, effective sigma less
No control on jet area
Full control on jet area with EDF, up to a limit

## Slide 4: Project Aims
Ducted Fan design for hover
Characterising Ducted Fan
Develop flying testbed
  Stability
  In-flight measurements

## Slide 6: Design Methods
Assumptions
  Isentropic flow
  No inlet/exit swirl
1D design
  SFME, SFEE
2D design
  Radial equilibrium
  Mixed vortex
  Sweep & lean
Axial velocity
Blade speed
Velocities
Flow angles
Chord distribution
Blade angles
Number of blades
Design Process
Notes: 1d design – rms value
Thought process
Mixed vortex .5 – will give more uniform chord as seen later

## Slide 7: Generating Blade Profiles
Absolute Velocities
Inputs
Φ, σ, Thrust, Geometry
Vx
Relative Velocities
(Rotor Plane)
(Stator Plane)

## Slide 8: Design Methods
Assumptions
  Isentropic flow
  No inlet/exit swirl
1D design
  SFME, SFEE
2D design
  Radial equilibrium
  Mixed vortex
  Sweep & lean
Axial velocity
Blade speed
Velocities
Flow angles
Chord distribution
Blade angles
Number of blades
Design Process
Inputs
Φ, σ, Thrust, Geometry
Notes: 1d design – rms value
Thought process
Mixed vortex .5 – will give more uniform chord as seen later

## Slide 9: Generating Blade Profiles
Absolute Velocities
Vx
Relative Velocities
(Rotor Plane)
(Stator Plane)

## Slide 10: Generating Blade Profiles
Use Lieblein correlation to set midspan chord
Use Carter’s empirical relation to set blade angles
Notes: Midline as basis!!
Midspan chord set by Lieblein DF
Midspan blade metal angles by Carter’s empirical relation from compressor cascade tests
Constant deviation across span sets rest of angles

## Slide 11: Generating Blade Profiles
Carter’s relation recalculates chord distribution
Lieblein correlation recalculates diffusion factor
Notes: Chord recalculated based on constant deviation (Carter’s rule)
Diffusion Factor recalculated across span according to Lieblein’s correlation

## Slide 12: Chosen Design
Sweep & Lean
Adding sweep and lean minimizes end-wall losses
Notes: Rotor-stator, long intake and moderate diffuser
Stator takes out swirl
Printing!!!!
Static tests, ch’ic perf
Reduce corner sep and trailing edge los

## Slide 13: Chosen Design
Flow coefficient |  | 0.80
Thrust |  | 10 N
Casing radius |  | 60 mm
Hub radius |  | 20 mm
Diffusion factor |  | 1.1
Flow coefficient |  | 0.80
Thrust |  | 10 N
Casing radius |  | 60 mm
Hub radius |  | 20 mm
Diffusion factor |  | 1.1
De Haller number = 0.85 Stall limit = 0.72
Notes: High phi means lower RPM

## Slide 14: Measuring Thrust, RPM, Pressure, Power
Pic of thing
Notes: Overview of interfacing with

## Slide 15: Thrust Measurement
Thrust
Data Collection
Raspberry Pi
SSH over WiFi
Shear Loadcell
Notes: Loadcell calibration
Secure shell

## Slide 16: RPM Measurement
RPM
Data Collection
Raspberry Pi
SSH over WiFi
RPM Sensor
Notes: Secure shell

## Slide 17: Pressure Measurement
Data Collection
DSA Pressure Transducer
Ethernet
DSA
Notes: From this, coupled with RPM, can work out phi and psi

## Slide 18: Power Measurement
Data Collection
QGroundControl
Telemetry
Power
Notes: Same computer terminal

## Slide 19: Validating Ducted Fans against Propellors
Ducted fan yields 64% increase in Figure of Merit
Notes: Not accounting for system efficiency

## Slide 20: Obtaining Ducted Fan Characteristic by Varying σ
Needs recollecting
Notes: Stall
Temperature sensitivity
Mention diffusion ducts
Includes spanwise variation due to vortex exponent
Once this is obtained, can obtain OP from flight through knowing RPM, technically SFME gives Vx for hover

## Slide 21: Inaugural Whittle Lab Test Flight!!
Notes: Needs renaming

## Slide 22: Now we have flying
Capacity to remotely measure:
  Power
  RPM
  Pressures
  Stability

## Slide 23: Conclusions
So far:
Designed and manufactured 4x EDFs
Proved a 64% increase in FOM for Ducted Fans compared to propellors
Obtained a characteristic for the Ducted Fan
Developed a flying testbed
Going forward:
Ready to improve testbed and use next term
Develop existing EDF design according to work by Jonathan Collins

## Slide 25: Backup slides
Inlet separation
Lining up stability with aero perf

## Slide 26: Slides + notes
What is my project – quad vs prop, ‘is better’
FOM – quantify, hover perf etc
Project aims – flying testbed, controllability, characterise
Assumptions/Methods – zero swirl, also incl 1D CV, FOM contour, de Haller number
Design build-up – flow, need carter to get blade chord, need diffusion fac to get blah blah
Pictures of design – variables, arrows to lean/sweep
Setup
FOM
Chic
Video
Conc
Backup
If it’s not on the slide, ur not allowed to mention it
Have an ending message at the bottom of each slide

## Slide 27: Structure
Intro and motivations (2-3 mins)
Present setup, method (1-2 mins)
  Mention FOM
Display results (2 mins)
  FOM comparison (ND) with props and edf at different rpms
  Ch’ic of EDF
Play video and discuss (1 min)
Conclude and present next steps (2 mins)

## Slide 28: What, How, Why
Currently propellors, but EDFs have multiple performance benefits
Design and build a VTOL EV with ducted fans for propulsors
Have a flying testbed to simulate various test cases – ref 5 stage flight
Can also assess trade-offs between number of propulsors and size
Fan can be characterised, so operating point can be easily obtained

## Slide 29: What have I done this term
Familiarised self with existing MATLAB design code to design new propulsor - updated areas where necessary (eg adding sweep/lean, creating stator holes)
Successfully operated static rig with all interfaces working
Repaired drone chassis, designed new connecting arms, fiddled with printing too many times
Collected performance results from different designs, attempted to produce ch’ic by varying sigma (WORK TO DO HERE)
Confirmed FOM improvement from prop to EDF
Adapted design to accommodate new motors
Built up drone to fly with 4x EDF’s

## Slide 30: Vortex Exponent
SDG: 1 = free, -1 = forced

## Slide 31
The Take-Off of e-VTOL
Ducted Fans
Higher thrust
Less Noise
Contained (Safer)
BUT
Do they work at a SYSTEM level?
Notes: The e-VTOL market has exploded in the past few years and is projected to continue growing, trebling by 2024.
The market shows us that no one configuration is being sought after, with a vast array of designs put forward
  PRIMARILY
  PROPELLERS
  DUCTED FANS
Ina static test, a ducted fan has a higher thrust output, is less noisy and is contained, meaning it is safer.
However does the cost of weight and stability prevent them from being a better propulsion system?
How we can determine whether ducted fans are a viable system solution to the e-VTOL propulsion problem>

## Slide 32: Project Questions
Are ducted fans more efficient in static hover?
Are ducted fans dynamically stable in an e-VTOL application?
Notes: This problem has two primary facets, arising from
  A static analysis
  A dynamic analysis
Firstly, the ducted fan as a system must be more efficient than a standard propeller in a static hovering configuration. Does the reduction in power requirement outweigh the increase in weight of the vehicle? Hence, ‘Are they a more efficient SYSTEM for e-VTOL vehicles?’
Secondly, the dynamic feasibility of the ducted fan is to be considered. How does the performance vary when the vehicle is subjected to lateral manoeuvres? Hence, ‘Are ducted fans FEASIBLE for an e-VTOL APPLICATION?’

## Slide 33: Are ducted fans more efficient in static hover?
Does added efficiency outweigh weight penalty for a simple light-weight design?
Hover tests with variable payload
Quadcopter propulsors compared:
  Generic off-the-shelf propeller
  APC e-VTOL optimised propeller
  Ducted Fan (??)
Notes: Changing a propulsor from a propeller to a ducted fan introduces a significant increase in weight.
The design must therefore be weight minimized, however, does the increase in performance outweigh the extra weight required?
Tests will be conducted with various payloads to determine performance across the fan characteristic.
Need to design a ducted fan suitable for this test.

## Slide 34: A Superior Figure of Merit
Notes: Need to quantify performance, SOMETHING TO MAXIMISE
Figure of Merit is a non-dimensional thrust to power ratio for a propulsor with zero freestream velocity, ie HOVER.
An ideal ducted fan can be shown to have a larger figure of merit than an open-rotor propeller, but this comes at the price of weight.
The diagram shows that an ideal propeller has a maximum FoM of 1. This is an absolute limit.
However, the ducted fan has another degree of freedom, the exit area of the diffuser can be varied and set (shown here as A_E). This control over flow area results in a FoM that has a dependence on the diffusion factor (SIGMA, defined here by A_E/A). This means an ideal ducted fan with a 1:1 diffuser has a FoM of 1.4, even without any diffusion.
Hence, how can the ducted fan be designed to maximise FoM in a system with a diffusion factor limited by both length and weight?
EXTRA
PROPELLER MODEL
  Velocity actuator
  Exit area NOT EQUAL to prop area (ie SMALL but non-unity FPR)
  EXIT pressure equal to atmospheric
  Consider ENERGY and MOMENTUM to get expression for area ratio

## Slide 35: Reduction of Free Variables
Floating Variables
Fixed Variables
Notes: The ducted fan has a broad design space that can be characterized by two variables, flow coefficient and stage loading (PHI and PSI)
The remaining variables have been fixed, either inherently by definition (sigma phi psi)
  OR by geometric constraints (r_h)
  OR by electrical limits (OMEGA)
However, there is no direct limit on the casing radius?
To close the problem, the thrust produced must be equal to the vehicle weight. I developed a mass model to relate both these quantities to the casing radius, and solving this problem at each design point, obtained the critical operating point for each.

## Slide 36: Reduction of Free Variables
Floating Variables
Fixed Variables
Motor Radius
Notes: The ducted fan design has a broad design space that can be characterized by two variables, flow coefficient and stage loading (PHI and PSI)
The remaining variables have been fixed, either inherently by definition (sigma phi psi)
  OR by geometric constraints (r_h)
  OR by electrical limits (OMEGA)
However, there is no direct limit on the casing radius?
To close the problem, the thrust produced must be equal to the vehicle weight. I developed a mass model to relate both these quantities to the casing radius, and solving this problem at each design point, obtained the critical operating point for each.

## Slide 37: Reduction of Free Variables
Floating Variables
Fixed Variables
Notes: The ducted fan design has a broad design space that can be characterized by two variables, flow coefficient and stage loading (PHI and PSI)
The remaining variables have been fixed, either inherently by definition (sigma phi psi)
  OR by geometric constraints (r_h)
  OR by electrical limits (OMEGA)
However, there is no direct limit on the casing radius?
To close the problem, the thrust produced must be equal to the vehicle weight.
I developed a mass model to relate both these quantities to the casing radius. Solving this problem at each design point obtains the critical operating r_c for design.

## Slide 38: Maximise Figure of Merit, Minimise Power
Increasing
Notes: I developed this model to maximise FoM and Minimise power.
The diagram shows the power required at each design point.
There are limits shown.
  The red line is a cuirrent limit for the motor
  The Solid black line is the limit of diffusion factor =1
  The dashed balck line is a geometric limit of diffusor symmetry.
This suggest we push the design towards the bottom left to reduce power.

## Slide 39: Minimise Power… What a big fan you have
Notes: This slide shows the variation in casing radius across the design space.
Previously, we determined the bottom left is the ideal design region however, this shows those designs to be too large.
Therefore I have chosen a design in the middle of this region

## Slide 40: Chosen Design
Flow coefficient |  | 0.80
Stage loading |  | 0.20
Casing radius |  | 57.7 mm
Fan speed |  | 7500 RPM
Diffusion factor |  | 1.26
Flow coefficient |  | 0.80
Stage loading |  | 0.20
Casing radius |  | 57.7 mm
Fan speed |  | 7500 RPM
Diffusion factor |  | 1.26
Notes: From my model, I have chosen this design.
A conservative diffuser and intake is used, that will be improved by the work Megan is going to talk about.

## Slide 41: Preliminary Propeller Data – The Baseline
Power vs Thrust
Constant wrt
Notes: The fan performnce will be compared against propeeller performance.
I have so far collected data for the propeller, shown here.
This shows teh propeller to have a constant FoM at various loads as expected. This FoM is fairly low as it is for an unoptimised propeller
I expect to see the hover optimized propeller closer to but still below 1, and the fan to be somewhere between 1 and 1.5
I will now talk about the dynamic aspect of the test.

## Slide 42: Are ducted fans FEASIBLE in an e-VTOL application?
Vehicle Velocity
Does the intake duct reduce dynamic stability during manoeuvres?
Small horizontal manoeuvres of varying amplitude
Dynamic stability determined:
  Does separation occur at intake?
  Does control system remain stable?
Notes: Now the fan has been developed, the next question is that of dynamic performance,?
The primary concern here is how the fan behaves in a crosswind, a common flow feature for a vehicle transitioning from hover to horizontal flight. (AS IN THE DIAGRAM)
Crosswinds can lead to separation and resulting decrease in performance AS WELL as destabilising moments on the vehicle.
THEREFORE the key questions are
  Does separation occur?
  Does the vehicle remain stable?
A test bed is needed to determine this

## Slide 43
Modular Dynamic Test Bed
Data Logging and Flight Control
Detachable Propulsor Assembly
(Ducted Fan or Prop)
Work completed as part of UROP
  Light-weight 3D printed parts (PLA)
  Modular
  Pixhawk4 flight hardware
  Bespoke chassis
Additional Michaelmas work
  RaspberryPi based on-board, real-time sensor hub
  Sensor design, development and integration
Notes: Here we see this test bed,
It has a cocentral data logging and flight control chassis,
as well as modular limbs and propulsor assemblies that are suitable for both ducted fans as well as propellers.
My design was 3D printed at the Whittle, allowing for rapid prototyping, also allowing the design to be as light as possible in my price-range (no carbon yet, sadly).
I have integrated flight control systems with a custom sensor management unit to provide on-board data logging and autonomous flight control.
This test bed allows all the required metrics to be determined…

## Slide 44: Data Collection, Control and Conclusions
Figure of Merit
  Power (Electrical, RPM, calibration)
  Thrust
Flow separation at intake
  Pressure Transducers
Control system stability
  6-DoF inertial sensors
  3 position sensors
Pixhawk4 Flight Controller
RPi3 A+ Sensor Management
Power Module (PM07)
RPM Sensors
ADC Breakout
Pressure Transducers
ESC
Motor Assembly
Ultrasound Proximity Sensors
Laptop
ONBOARD
Notes: An overview of the system
Two main aspects to testing this way. The first is Control and the second is Data Collection.
This graphic shows the system level interactions involved.
  Managing the vehicle as a whole is a laptop
  The control aspect is handled by a Pixhawk4 Flight Controller that manages the stability of the platform.
  Power and Motor control is shown on the LHS
  The RHS shows the sensors and the RPi sensor hub.
I have developed a Raspberry Pi based sensor management unit that can record and transmit data. It includes up to 8-channel ADC that allows multi-stream data-logging remotely or on-board.
Sensors are integrated with the existing flight software to enable autonomous position control.
They allow both static and dynamic performance to be determined. These are shown on the left.
  Figure of Merit is determined from Power and Thrust measurements
  Flow separation comes from tappings and pressure transduces at the intake
  Control stability can be determined from the flight control system
Using this test platform, I will be able to determine the performance of the fan in both a static AND dynamic context NExt term .
THANK YOU

## Slide 45
Notes: Back up slides
ESDU
LOW RE PROFILES FROM MATHEW M PAPER (DYSON)

## Slide 46: Mass Model
Diffusor angle limited by flow separation
Notes: When considering the mass model, a hidden fixed geometric variable, diffuser length, is set by the maximum angle of the diffuser from the axial flow direction.
The constants shown here are obtain from empirically obtained data in ESDU 75026 and represent a conservative limit on diffuser separation.
The equation shows that this limit can be expressed solely in terms of SIGMA (diffusion ratio) and hence the operating point variables PHI and PSI.