## Slide 1: e-VTOL Flying Testbed
Sam Drury
03/12/2020
Supervisor:
Dr Sam Grimshaw
Whittle Laboratory
https://www.bellflight.com/products/bell-nexus

## Slide 2: Benefits of Ducted Fans vs Propellors
Ducted Fans can improve hovering performance compared to propellors while being safer and quieter

## Slide 3: Devising a Suitable Performance Metric

## Slide 4: Project Aims
Ducted Fan design for hover
Characterising Ducted Fan
Develop flying testbed
  Stability
  In-flight measurements

## Slide 5: Design Methods
Assumptions
  Isentropic flow
  No inlet/exit swirl
1D design
  SFME, SFEE
2D design
  Radial equilibrium
  Mixed vortex
  Sweep & lean
Axial velocity
Blade speed
Velocities
Flow angles
Chord distribution
Blade angles
Number of blades
Design Process
V1

## Slide 6: Generating Blade Profiles
Absolute Velocities
Inputs
Φ, σ, Thrust, Geometry
Vx
Relative Velocities
(Rotor Plane)
(Stator Plane)
V1

## Slide 7: Design Methods
Assumptions
  Isentropic flow
  No inlet/exit swirl
1D design
  SFME, SFEE
2D design
  Radial equilibrium
  Mixed vortex
  Sweep & lean
Axial velocity
Blade speed
Velocities
Flow angles
Chord distribution
Blade angles
Number of blades
Design Process
Inputs
Φ, σ, Thrust, Geometry
V2

## Slide 8: Generating Blade Profiles
Absolute Velocities
Vx
Relative Velocities
(Rotor Plane)
(Stator Plane)
V2

## Slide 9: Generating Blade Profiles
Use Lieblein correlation to set midspan chord
Use Carter’s empirical relation to set blade angles

## Slide 10: Generating Blade Profiles
Carter’s relation recalculates chord distribution
Lieblein correlation recalculates diffusion factor

## Slide 11: Chosen Design
Sweep & Lean
Adding sweep and lean minimizes end-wall losses

## Slide 12: Chosen Design
Flow coefficient |  | 0.80
Thrust |  | 10 N
Casing radius |  | 60 mm
Hub radius |  | 20 mm
Diffusion factor |  | 1.1
Flow coefficient |  | 0.80
Thrust |  | 10 N
Casing radius |  | 60 mm
Hub radius |  | 20 mm
Diffusion factor |  | 1.1
De Haller number = 0.85 Stall limit = 0.72

## Slide 13: Measuring Thrust, RPM, Pressure, Power
Pic of static test rig

## Slide 14: Thrust Measurement
Thrust
Data Collection
Raspberry Pi
SSH over WiFi
Shear Loadcell

## Slide 15: RPM Measurement
RPM
Data Collection
Raspberry Pi
SSH over WiFi
RPM Sensor

## Slide 16: Pressure Measurement
Data Collection
DSA Pressure Transducer
Ethernet
DSA

## Slide 17: Power Measurement
Data Collection
QGroundControl
Telemetry
Power

## Slide 18: Validating Ducted Fans against Propellors
Ducted fan yields 64% increase in Figure of Merit

## Slide 19: Obtaining Ducted Fan Characteristic by Varying σ
Needs recollecting

## Slide 20: Inaugural Whittle Lab Test Flight!!

## Slide 21: Now we have flying
Capacity to remotely measure:
  Power
  RPM
  Pressures
  Stability

## Slide 22: Conclusions
So far:
Designed and manufactured 4x EDFs
Proved a 64% increase in FOM for Ducted Fans compared to propellors
Obtained a characteristic for the Ducted Fan
Developed a flying testbed
Going forward:
Ready to improve testbed and use next term
Develop existing EDF design according to work by Jonathan Collins