## Slide 1: Propulsion Systems for e-VTOL aircraft
Sam Drury
04-11-2020 Progress Update
Supervisor:
Dr Sam Grimshaw
Whittle Laboratory

## Slide 2: Progress
Design
Numerous tweaks to increase print performance
Rotor and stator printed
Rig
Successful comms for RPM, thrust, input power (V & I)
Still to connect DSA
Planning
Assess performance characteristics of flying testbed first
Leaning towards quantifying cruise performance
Results obtained!
Markham Wind Tunnel?
CFD iterations to validate current model
Drone – Fan connection still to be sourced/created
Notes: Not two weeks worth of progress
Tweaks – stator holes
Other ideas
Remain with hover, optimise and look at
Investigate noise vs blade number

## Slide 3: Printed Design
Notes: Changes since last iteration
Thicker stators to accommodate wire (marginally)
Chord increased to utilise space and minimise rotor-stator distance

## Slide 4: Design Performance
Notes: Larger chord, maximise space
Large rotor sweep at hub (geometric constraints)

## Slide 5: Results
(nice graph here, maybe bar chart – log RPM, thrust, power, Mf, )

## Slide 6: Concerns
Synchronous vibration of rotor
Axial movement in motor
Outsource stator prints, machine rotors from plastic block
Effect of blade count unknown
Increase validity of results through using same motor
Iterate various designs through CFD prior to outsourcing / machining?
Outside flying challenges
(enter solution here)
Notes: (and general printing issues)
Outside flying
Interfacing to do remote hover
  RPi records loadcell (don’t need) and RPM (need)
Allow drone to traverse
ALSO! Broken lug 

## Slide 7: Week 5 Plans
(Test existing design?)
Vary inlet/outlet to assess any performance change
  Low HTR design at low Re (JSE demonstrated off-design results)
Continue investigating literature
Cement premise of project
Notes: JSE – high psi, lower phi, hence much lower sigma

## Slide 8: MATLAB Design using SDG Code
Flow coefficient |  | 0.80
Casing radius |  | 60 mm
R_Lean | ° | 20
R_Sweep | ° | 4
Area ratio |  | 1.1
Thrust | T | 10 N
Stage loading (tt) |  | 0.265
Fan speed |  | 7977 RPM
Blades [R,S] |  | [11,10]
Flow coefficient |  | 0.80
Casing radius |  | 60 mm
R_Lean | ° | 20
R_Sweep | ° | 4
Area ratio |  | 1.1
Thrust | T | 10 N
Stage loading (tt) |  | 0.265
Fan speed |  | 7977 RPM
Blades [R,S] |  | [11,10]
Inputs
Outputs
Notes: High thrust, but reducing this brings fan speed down eg 6N gives 6200 rpm
Also sensitive to area ratio: sigma of 1 gives 7600 rpm

## Slide 9: Performance Overview
Notes: Notable points:
Sensible triangles/shape
Constant deviation, to ensure correlation at large HTR’s doesn’t blow up (this can be changed to give constant DF, but not much shape difference)
Little chord variation
Very 2D stator

## Slide 10: Adding Sweep and Lean
Sweep
Parabolic, quadratic
4°
Lean
Parabolic, quartic
20°
Radial view from annulus
U
Suitable values chosen from Taylor & Miller (2015)
Notes: Sweep – side-on
Lean – front-on

## Slide 11: Finalised Rotor
Notes: Lots of altering .ibl file to ensure CAD fit

## Slide 12: MATLAB to .stl for 3D Printer
Matlab
Press run
Output .ibl for rotor and stator
Creo
Change curves to new .ibl file
Regenerate
OPTIONAL: Save .ibl files under separate name
Reselect curves
Save as .stl

## Slide 13: Week 3 Plans
Tweak design if necessary
Print 4x rotors
  Check whether stators, shrouds etc also need printing
Continue exploring literature

## Slide 14
The Take-Off of e-VTOL
Ducted Fans
Higher thrust
Less Noise
Contained (Safer)
BUT
Do they work at a SYSTEM level?
Notes: The e-VTOL market has exploded in the past few years and is projected to continue growing, trebling by 2024.
The market shows us that no one configuration is being sought after, with a vast array of designs put forward
  PRIMARILY
  PROPELLERS
  DUCTED FANS
Ina static test, a ducted fan has a higher thrust output, is less noisy and is contained, meaning it is safer.
However does the cost of weight and stability prevent them from being a better propulsion system?
How we can determine whether ducted fans are a viable system solution to the e-VTOL propulsion problem>

## Slide 15: Project Questions
Are ducted fans more efficient in static hover?
Are ducted fans dynamically stable in an e-VTOL application?
Notes: This problem has two primary facets, arising from
  A static analysis
  A dynamic analysis
Firstly, the ducted fan as a system must be more efficient than a standard propeller in a static hovering configuration. Does the reduction in power requirement outweigh the increase in weight of the vehicle? Hence, ‘Are they a more efficient SYSTEM for e-VTOL vehicles?’
Secondly, the dynamic feasibility of the ducted fan is to be considered. How does the performance vary when the vehicle is subjected to lateral manoeuvres? Hence, ‘Are ducted fans FEASIBLE for an e-VTOL APPLICATION?’

## Slide 16: Are ducted fans more efficient in static hover?
Does added efficiency outweigh weight penalty for a simple light-weight design?
Hover tests with variable payload
Quadcopter propulsors compared:
  Generic off-the-shelf propeller
  APC e-VTOL optimised propeller
  Ducted Fan (??)
Notes: Changing a propulsor from a propeller to a ducted fan introduces a significant increase in weight.
The design must therefore be weight minimized, however, does the increase in performance outweigh the extra weight required?
Tests will be conducted with various payloads to determine performance across the fan characteristic.
Need to design a ducted fan suitable for this test.

## Slide 17: A Superior Figure of Merit
Notes: Need to quantify performance, SOMETHING TO MAXIMISE
Figure of Merit is a non-dimensional thrust to power ratio for a propulsor with zero freestream velocity, ie HOVER.
An ideal ducted fan can be shown to have a larger figure of merit than an open-rotor propeller, but this comes at the price of weight.
The diagram shows that an ideal propeller has a maximum FoM of 1. This is an absolute limit.
However, the ducted fan has another degree of freedom, the exit area of the diffuser can be varied and set (shown here as A_E). This control over flow area results in a FoM that has a dependence on the diffusion factor (SIGMA, defined here by A_E/A). This means an ideal ducted fan with a 1:1 diffuser has a FoM of 1.4, even without any diffusion.
Hence, how can the ducted fan be designed to maximise FoM in a system with a diffusion factor limited by both length and weight?
EXTRA
PROPELLER MODEL
  Velocity actuator
  Exit area NOT EQUAL to prop area (ie SMALL but non-unity FPR)
  EXIT pressure equal to atmospheric
  Consider ENERGY and MOMENTUM to get expression for area ratio

## Slide 18: Reduction of Free Variables
Floating Variables
Fixed Variables
Notes: The ducted fan has a broad design space that can be characterized by two variables, flow coefficient and stage loading (PHI and PSI)
The remaining variables have been fixed, either inherently by definition (sigma phi psi)
  OR by geometric constraints (r_h)
  OR by electrical limits (OMEGA)
However, there is no direct limit on the casing radius?
To close the problem, the thrust produced must be equal to the vehicle weight. I developed a mass model to relate both these quantities to the casing radius, and solving this problem at each design point, obtained the critical operating point for each.

## Slide 19: Reduction of Free Variables
Floating Variables
Fixed Variables
Motor Radius
Notes: The ducted fan design has a broad design space that can be characterized by two variables, flow coefficient and stage loading (PHI and PSI)
The remaining variables have been fixed, either inherently by definition (sigma phi psi)
  OR by geometric constraints (r_h)
  OR by electrical limits (OMEGA)
However, there is no direct limit on the casing radius?
To close the problem, the thrust produced must be equal to the vehicle weight. I developed a mass model to relate both these quantities to the casing radius, and solving this problem at each design point, obtained the critical operating point for each.

## Slide 20: Reduction of Free Variables
Floating Variables
Fixed Variables
Notes: The ducted fan design has a broad design space that can be characterized by two variables, flow coefficient and stage loading (PHI and PSI)
The remaining variables have been fixed, either inherently by definition (sigma phi psi)
  OR by geometric constraints (r_h)
  OR by electrical limits (OMEGA)
However, there is no direct limit on the casing radius?
To close the problem, the thrust produced must be equal to the vehicle weight.
I developed a mass model to relate both these quantities to the casing radius. Solving this problem at each design point obtains the critical operating r_c for design.

## Slide 21: Maximise Figure of Merit, Minimise Power
Increasing
Notes: I developed this model to maximise FoM and Minimise power.
The diagram shows the power required at each design point.
There are limits shown.
  The red line is a cuirrent limit for the motor
  The Solid black line is the limit of diffusion factor =1
  The dashed balck line is a geometric limit of diffusor symmetry.
This suggest we push the design towards the bottom left to reduce power.

## Slide 22: Minimise Power… What a big fan you have
Notes: This slide shows the variation in casing radius across the design space.
Previously, we determined the bottom left is the ideal design region however, this shows those designs to be too large.
Therefore I have chosen a design in the middle of this region

## Slide 23: Chosen Design
Flow coefficient |  | 0.80
Stage loading |  | 0.20
Casing radius |  | 57.7 mm
Fan speed |  | 7500 RPM
Diffusion factor |  | 1.26
Flow coefficient |  | 0.80
Stage loading |  | 0.20
Casing radius |  | 57.7 mm
Fan speed |  | 7500 RPM
Diffusion factor |  | 1.26
Notes: From my model, I have chosen this design.
A conservative diffuser and intake is used, that will be improved by the work Megan is going to talk about.

## Slide 24: Preliminary Propeller Data – The Baseline
Power vs Thrust
Constant wrt
Notes: The fan performnce will be compared against propeeller performance.
I have so far collected data for the propeller, shown here.
This shows teh propeller to have a constant FoM at various loads as expected. This FoM is fairly low as it is for an unoptimised propeller
I expect to see the hover optimized propeller closer to but still below 1, and the fan to be somewhere between 1 and 1.5
I will now talk about the dynamic aspect of the test.

## Slide 25: Are ducted fans FEASIBLE in an e-VTOL application?
Vehicle Velocity
Does the intake duct reduce dynamic stability during manoeuvres?
Small horizontal manoeuvres of varying amplitude
Dynamic stability determined:
  Does separation occur at intake?
  Does control system remain stable?
Notes: Now the fan has been developed, the next question is that of dynamic performance,?
The primary concern here is how the fan behaves in a crosswind, a common flow feature for a vehicle transitioning from hover to horizontal flight. (AS IN THE DIAGRAM)
Crosswinds can lead to separation and resulting decrease in performance AS WELL as destabilising moments on the vehicle.
THEREFORE the key questions are
  Does separation occur?
  Does the vehicle remain stable?
A test bed is needed to determine this

## Slide 26
Modular Dynamic Test Bed
Data Logging and Flight Control
Detachable Propulsor Assembly
(Ducted Fan or Prop)
Work completed as part of UROP
  Light-weight 3D printed parts (PLA)
  Modular
  Pixhawk4 flight hardware
  Bespoke chassis
Additional Michaelmas work
  RaspberryPi based on-board, real-time sensor hub
  Sensor design, development and integration
Notes: Here we see this test bed,
It has a cocentral data logging and flight control chassis,
as well as modular limbs and propulsor assemblies that are suitable for both ducted fans as well as propellers.
My design was 3D printed at the Whittle, allowing for rapid prototyping, also allowing the design to be as light as possible in my price-range (no carbon yet, sadly).
I have integrated flight control systems with a custom sensor management unit to provide on-board data logging and autonomous flight control.
This test bed allows all the required metrics to be determined…

## Slide 27: Data Collection, Control and Conclusions
Figure of Merit
  Power (Electrical, RPM, calibration)
  Thrust
Flow separation at intake
  Pressure Transducers
Control system stability
  6-DoF inertial sensors
  3 position sensors
Pixhawk4 Flight Controller
RPi3 A+ Sensor Management
Power Module (PM07)
RPM Sensors
ADC Breakout
Pressure Transducers
ESC
Motor Assembly
Ultrasound Proximity Sensors
Laptop
ONBOARD
Notes: An overview of the system
Two main aspects to testing this way. The first is Control and the second is Data Collection.
This graphic shows the system level interactions involved.
  Managing the vehicle as a whole is a laptop
  The control aspect is handled by a Pixhawk4 Flight Controller that manages the stability of the platform.
  Power and Motor control is shown on the LHS
  The RHS shows the sensors and the RPi sensor hub.
I have developed a Raspberry Pi based sensor management unit that can record and transmit data. It includes up to 8-channel ADC that allows multi-stream data-logging remotely or on-board.
Sensors are integrated with the existing flight software to enable autonomous position control.
They allow both static and dynamic performance to be determined. These are shown on the left.
  Figure of Merit is determined from Power and Thrust measurements
  Flow separation comes from tappings and pressure transduces at the intake
  Control stability can be determined from the flight control system
Using this test platform, I will be able to determine the performance of the fan in both a static AND dynamic context NExt term .
THANK YOU

## Slide 28
Notes: Back up slides
ESDU
LOW RE PROFILES FROM MATHEW M PAPER (DYSON)

## Slide 29: Mass Model
Diffusor angle limited by flow separation
Notes: When considering the mass model, a hidden fixed geometric variable, diffuser length, is set by the maximum angle of the diffuser from the axial flow direction.
The constants shown here are obtain from empirically obtained data in ESDU 75026 and represent a conservative limit on diffuser separation.
The equation shows that this limit can be expressed solely in terms of SIGMA (diffusion ratio) and hence the operating point variables PHI and PSI.